## Slide 1: Multi-Hazard Resilience Quantification for Civil Infrastructure Systems
Elise Miller-Hooks
University of Maryland
www.millerhooks.umd.edu
University of Maryland, October 22, 2014

## Slide 2: Graduate Student Contributors
Graduated
Lisa Chen, Ph.D.
Rahul Nair, Ph.D.
Hakob Avetisyan, Ph.D.
Reza Faturechi, Ph.D.
Xiaodong Zhang, Ph.D.
Continuing
Mercedeh TariVerdi
Ali Asadabadi
Neza Vodopivec
Hossein Fotouhi
Kevin Denny (UG)

## Slide 3: Two Components of Resilience
Inherent
  Inherent capability to absorb or cushion effects of disaster via its topological and operational attributes
Adaptive
  Potential cost-effective, immediate actions that can be taken to preserve or restore system’s ability to perform its intended function in disaster’s aftermath

## Slide 4: 3 Applications 3 Concepts
Intermodal Goods Transport (adaptability)
Airport Taxiway and Runway Systems (preparedness, adaptability)
Drivers – Roadway Travel Time (disaster life cycle)

## Slide 5: Application 1: Intermodal Freight Transport
s.t.
Maximize expected throughput over all scenarios
Total flow along all paths cannot exceed demand
At most one recovery action in each link
Binary and integrality constraints
Links cannot support flows exceeding capacity
Level-of-service constraint
Budget constraint on recovery activities

## Slide 6: Solution
(P) can be decomposed into a set of independent deterministic programs (P(x)), one for each realization, x
Each deterministic program represents an NP-hard problem containing a large number of variables
  Proof by reduction from knapsack problem
Exact solution via
  Benders decomposition
  Column generation for subproblem solution
  Monte Carlo simulation with spatial and temporal dependencies for generating scenarios

## Slide 7: Port of Świnoujście, Poland
Focus on IM nodal facility
  High proportion of cargo transit time is spent at nodal facilities
  Bulk, container terminal and Ro/Ro operations

## Slide 8: Port of Świnoujście, Poland
PORT
Sweden
Denmark
Germany
(Berlin 140 km)
Czech Rep.
(Prague 533 km)
Slovakia
(Bratislava 783 km)
Poland
(Poznan 234 km)
(Wroclaw 371 km)
ferries
road and rail
Rest of Europe
cargo ships

## Slide 10: Network Representation
Processes = capacitated link
Physical infrastructure & processes

## Slide 11: Disruption Scenarios
Scenario defined by location, intensity, and impact: uncertain
Disasters impact processes and reduce link capacities
Terrorism
(bomb)
Terrorism
(hinterland
access)
Terrorism
(coordinated/arson
-near chemical storage)
Earthquake
Local Flooding

## Slide 12: Some Details
Additional Input
  Recovery activities and their impact on various links and processes
  Cargo flows through port
  Computational Experiments
  10,000 random realizations of disruptions and throughput measured
  Network
  10 O-D pairs
  164 arcs, 390 paths
  1261 recovery actions
  Total =$76.6 million
  Recovery budget
  $0-$100,000

## Slide 13: Results
Budget ($) | Resilience level
0 | 77%*
10,000 | 87%
50,000 | 97%
100,000 | 99%
Increase in resilience due solely to recovery actions
*Port services 77% of flows

## Slide 14: Point Resilience
Stabilization after ~2k realizations
      The higher the budget, the narrower the range

## Slide 15: Mitigation & Preparedness
Solution of (P) provides optimal recovery actions to take for monetary/time budgets
    Can take preparedness steps to facilitate recovery:
    Network expansion: e.g. add new link
    Retrofit – harden network components for greater resistance
    Order spare parts/backup equipment
    Preposition resources to aid anticipated recovery activities
    Implement technologies, training
Preparedness actions can enhance
    inherent coping capacity
    reduce time and cost of recovery actions

## Slide 16: Maximizing Resilience
First stage:
Maximize throughput in each scenario
Total flow along all paths cannot exceed demand
Budget constraint on preparedness and recovery activities
Links cannot support flows exceeding capacity
Level-of-service constraint
At most one recovery action in each link, integer/binary d.v.
Second stage:
At most one preparedness action in each link, binary d.v.
Maximize expected throughput

## Slide 17: Application 2: Airport Taxiway & Runway Pavement Networks
  Vulnerable to
    extreme climatic/geological events
    random operational events
    natural deterioration
    human-induced events
  Major damage types (asphalt/ concrete)
    cracking
    disintegration
    distortion
    loss of skid resistance - increased surface slipperiness
  Assess airport readiness to cope with damage

## Slide 18: Airport Resilience
System performance
Time
Disaster moment
Pre-event performance
Post-response performance
coping capacity
Adaptive capacity
Expectation of total flow of all aircraft types and maneuvers
Total demand

## Slide 19: Airport Capacity Estimation
Runway capacity estimation
    through capacity envelopes, boundaries of arrival and departure flows for each runway configuration (FAA 2004)
    Runway configuration g:
    Flow of maneuver w in runway a’ for configuration g
    Modeling parameters
    Individual runway a’:

## Slide 20: Airport Capacity Estimation
Taxiway capacity estimation
    piecewise linear envelopes, boundaries of taxiway bi-directional flow (using piecewise linearization of Sherali, 2001)
    Directional
    taxiway flows
    Convex-combination weights
    Taxiway capacity

## Slide 21: Minimum Operating Strip (MOS) Requirements
Runway segmentation to manage repair actions
Shortest set of consecutive functioning runway segments for safe landing and takeoff
Landing
7
6
5
4
3
2
1
Takeoff
7
1
6
5
4
3
2

## Slide 22: MOS Requirements
Constraints to capture max functioning runway length given segment damage states and repair actions
Min takeoff length requirement
Post-event damage state
Post-response damage state
4
3
2
1
4
3
2
1

## Slide 23: Optimization Model
Max. expected total arrival/departure flows over all ξ
1st stage decision
# of teams to train
2nd stage decision
Link/path flows (# of arrival/departure flights)
Runway configuration selection
# and type of equipment to purchase
Taxiway flow allowed if damage state equal to 1
Landing/takeoff min runway length requirements
Taxiway/runway post-repair damage state
Max allowed repair time
Repair actions with internal or external resources
Budgetary limitations
Non-negativity and integrality

## Slide 24: Envisioned DSS

## Slide 25: Modeling Input
Scenario generation
Identification of
  repair action types
  equipment requirements
  implementation time & costs
  external repair resources

## Slide 26: Illustrative Example
New York LaGuardia airport (LGA)
13
31
22
04

## Slide 27: Optimization Model Input
Runway configurations

## Slide 28: Optimization Model Input
Repair equipment list
Disruption types & possible consequences

## Slide 29: Modeling Results
Optimal budget allocation on internal/ external resources
Probability: runway configuration selection

## Slide 30: Modeling Results
Resilience indifference curves
0.75

## Slide 31: Application 3: Travel Time Resilience for Roadways
Travel time key in vehicular traffic
Challenge: how to model decentralized response of users to disruption?
Partial User-Equilibrium

## Slide 32: Information Evolution in Disaster
Disaster tree captures information evolution corresponding to decisions at each stage of the disaster life cycle

## Slide 33: Travel Time Resilience Problem TTRP
Bilevel, three-stage, stochastic program with PUE constraints
    Upper-Level (leader):
        Uncertainty unfolds
        Mitigation, preparedness and response actions identified/budgeted
    Lower-Level (follower):
        user response to UL decisions shortly after response stage, seeks PUE
    Extension of stochastic network design problem (SNDP), formulated as SMPEC
    Uncertainty in both levels
    Stackelberg equilibrium at optimality

## Slide 34: TTRP Formulation
  Upper-Level:
  Lower-Level (PUE):

## Slide 35: Progressive Hedging Algorithm (PHA - Rockefeller and Wets 1991)
  Address nonlinearities
  Nonlinear, convex objective
  Nonconvex constraints
  TTRP transformed to single-level, 3-stage SMIP
  KKT conditions
  PHA
  Lagrangian decomposition by scenario
  Global optimality guaranteed
  Non-anticipativity constraints added to force identical values over 3rd-stage information states
Nonanticipativity constraints

## Slide 36: Numerical Application
  90 multi-hazard scenarios

## Slide 37: RIPS II: Interdependency and Civil Infrastructure Societal Systems

## Slide 38
NSF RIPS II: Quantifying Disaster Resilience of Critical Infrastructure-based Societal Systems with Emergent Behavior and Dynamic Interdependencies
UMD-JHU-UDel

## Slide 39: A Civil Infrastructure-based Societal System (CIbSS)
Comprised of interdependent buildings that together serve a community function
Is dependent on networks of critical lifelines
Family of structures linked by occupancy type, people, policies, information, location, services
Dependent on human, organizational, political, transportation and cyber links

## Slide 40: Lifelines Loss & Component Downtime Assessment Input to System Performance
(S,P)ς
Performance
single system state

## Slide 41: Interpret and model adaptive actions, emerging organizational behaviors, changing policies: dynamic interdependencies

## Slide 42: Solution Framework

## Slide 43: Thank you
Peer-reviewed journal articles
Nair, R., H. Avetisyan and E. Miller-Hooks (2010). “Resilience of Ports, Terminals and Other Intermodal Components,” Transportation Research Record 2166, 54-65.
Chen, L. and E. Miller-Hooks (2012). “Resilience: An Indicator of Recovery Capability in Intermodal Freight Transport,” Transportation Science 46, 109-123.
Miller-Hooks, E., X. Zhang and R. Faturechi (2012). “Measuring and Maximizing Resilience of Freight Transportation Networks,” Computers and Operations Research 39(7), 1633–1643.
Faturechi, R. and E. Miller-Hooks (2014). “Disaster Resilience in Civil Infrastructure Systems: Quantification and Optimization,” Computer-Aided Civil and Infrastructure Engineering Systems 29, 572-589.
Faturechi, R., E. Levenberg and E. Miller-Hooks (2014). “Evaluating and Optimizing Resilience of Airport Pavement Networks,” Computers and Operations Research 43, 335–348.
Faturechi, R. and E. Miller-Hooks (2014). “Travel Time Resilience of Roadway Networks under Disaster,” Transportation Research Part B 70, 47-64.
Faturechi, R. and E. Miller-Hooks (in press). “A Comprehensive Review of the Literature on Disaster Performance Analysis of Transportation Systems,” in press in the ASCE Journal of Infrastructure Systems (available on-line).
Zhang, X. and E. Miller-Hooks (in press). “Scheduling Short-Term Recovery Activities to Maximize Transportation Network Resilience,” ASCE Journal of Computing in Civil Engineering.
Zhang, X., E. Miller-Hooks and K. Denny (in review). “The Role of Network Topology in Resilience of Transportation Systems,” in second round of reviews for publication in Journal of Transport Geography.